BASIC ATV SET UP ISTRUCTIONS

- REMOVE ATV FROM PACKAGING

- SEPERATE COMPONENTS INTO GROUPS i.e  NUTS AND BOLTS, TIRES AND ETC.

- PUT TIRES ON. USE BOLTS PROVIDED FOR EACH ONE 4 BOLTS ON EACH TIRE.

- GRAB HANDLE BAR ASSEMBLY THAT CAME IN SEPARATE BOX AND ATTACH HANDLE BARS. ADJUST TO YOUR COMFORT. 4 BOLTS TOTAL

- LOCATE BATTERY AND CLEAR BOTTLE OF ELECTROLITE. CUT THE TOP OFF BOTTLE. AND ADD ELECTROLITE IN TO BATTERY EVENLY. LET STAND FOR 15 MINTUES TO SELF CHARGE. NOTE CLEAR LIQUID IS ELECTROLITE AND REACTS WITH THE DRY CHARGE BATTERY. NO NEED TO CHARGE ON WALL.

- INSTALL BATTERY AT THE REAR OF THE ATV UNDERNEATH THE TAIL LIGHT. NOTE: GREEN GOES POSITVE RED GOES NEGATIVE OR RED GOES POSITIVE OR BLACK GOESD NEGATIVE. DIFFERENT SIZE ATV’S HAVE DIFFERENT WIRING.

- ADD GASOLINE.

- LOCATE THE PET COCK ( FUEL CUT OFF VAVLE) AND TURN ON.

- TURN ON CHOKE (UNDERNEATH GAS TANK UNDERNEATH CUT OFF VALVE)

- DO NOT START YET. FEATHER THE GAS THROTTLE TO GET GAS INTO THE CARBURATOR. CALLED PRIMING THE CARB. (FEATHER 10 TIMES BEFORE STARTING)

- INSERT KEY FLIP THE SWITCH TO THE ON POSITION WHILE FEATHERING THE GAS PUSH AND HOLD THE START BUTTON AND HOLD GAS HALF WAY TO WARM UP.

- WHEN ABLE SHUT OFF CHOKE AND SET IDLE.

NOTE: As stated on our website we aim to bring you safe affordable ATV’s at a price you have never seen before. Please make sure that all the connections are secure and safe. As stated on our website if you cannot perform the assy we suggest you hire a local tech to do it for you. Assy. is generally 100.00 and we can assist you in locating a tech. We have personally assembled all of the machines we sell and they are very easy. Really anyone with some mechanical ability can do it. There are very minimal steps to complete the assembly. Although there are not really instructions with the machine and never promised in the sale we will however try to assist you if you need assistance. If you have questions please email support@countyimports.com . Assembly will take 20-40 mins.