This is just some quick help tips for your Discovery 2:

- TD5 Discovery can’t get up to speed: Low fuel rail pressure, check fuel filter & pump

- TD5 Discovery surging, gearchange erratic: Check & clean inlet manifold air pressure sensor, or faulty turbo modulator

- Discovery 2 diff lock light comes on every time brake pedal is depressed or put into reverse: Replace stop lamp fuse (No.25)

- M+S (Mil Lamp) lights come on, goes into limp mode: Clean air flow meter

- Discovery 2 V8 runs for 20 minutes then conks out then won’t start for 10 or more minutes: Crank angle sensor overheating

- M+S lights: Gearbox inhibitor switch could be damaged by water (a/c drips on it)